## Slide 1
SANDISK HACKATHON · TEAM ASTERIX · 2026
UVM Configuration
Intelligence
Turning raw UVM simulation logs into ranked failure causes, deterministic-bug isolation, and a recommended configuration that is both fast and safe.
50,000
runs in the corpus
1.01 M
log lines parsed
2.0 s
full-corpus parse
0.88
risk-model ROC-AUC
Presented by ______________________ Reviewer ______________________
Notes: Opening line: verification teams drown in log volume but still triage failures by hand. This project reads the logs, finds which configuration combinations cause failures, separates real RTL bugs from seed noise, and recommends a safe configuration. Everything you will see runs end to end on a 50,000-run corpus.

## Slide 2
THE PROBLEM
Regression logs answer 'what', never 'why'
UVM Configuration Intelligence · Team Asterix
02
Where verification time goes today
A single nightly regression emits over a million log lines; triage is manual and does not scale.
A failing run reports that it failed — not which combination of knobs made it fail.
Seed-noise flakes and genuine deterministic RTL bugs look identical in a log file.
Config tuning is folklore: nobody can state the fastest setting that still meets a risk budget.
Ad-hoc scripts are written per debug session and thrown away — nothing accumulates.
01
Ingest at scale
Parse arbitrary UVM log dumps into structured run and error tables in seconds.
02
Rank the causes
Attribute failure risk to the configuration knobs an engineer can actually set.
03
Isolate real bugs
Separate deterministic RTL failures from seed-dependent noise, automatically.
04
Recommend a config
Maximise throughput subject to an explicit predicted-risk ceiling.
Notes: Frame the pain first, then the four objectives. Each objective maps to a component you will see later: parser, risk model, fingerprinting, recommender.

## Slide 3
SOLUTION OVERVIEW
Six stages, one upload, one report
Drop .log files on the dashboard — the whole chain runs on a worker thread and streams progress back to the UI.
UVM Configuration Intelligence · Team Asterix
03
01
Log ingestion
Single-pass parser with startswith guards ahead of any regex. 1,015,872 lines in 2.0 s, zero malformed blocks.
02
Failure-risk model
LightGBM on configuration knobs only, explained with SHAP TreeExplainer. Global ranking plus per-value attribution.
03
Failure fingerprinting
Error text masked to seed-invariant templates, TF-IDF + DBSCAN clustering, determinism score per cluster.
04
Trade-off frontier
Pareto frontier over throughput versus predicted risk, grouped on the top SHAP-ranked discrete settings.
05
Recommender
Optuna TPE over two surrogates — risk classifier and pass-only throughput regressor — under a 2 % risk ceiling.
06
Config diff
Aggregate pass/fail distribution shift plus nearest-twin diffing that names the exact settings that flipped.
Every stage is wrapped independently — if one fails, the rest of the report still renders and the failure is recorded in the stage log rather than killing the job.
Notes: Stress the fault isolation line at the bottom — it is a real engineering decision, not a slogan.

## Slide 4
SYSTEM ARCHITECTURE
Upload → parse → fan-out → one JSON payload
UVM Configuration Intelligence · Team Asterix
04
React 18 + Vite UI
dropzone · polling · 7 tabs
FastAPI service
/analyze · /jobs · /runs · /diff
Worker thread
job registry · progress callback
uvm_intel.log_parser — single pass, shared grammar with the generator
runs frame (config + metrics + verdict) · errors frame (severity, component, tag, masked template)
risk_model
LightGBM + SHAP
fingerprints
TF-IDF + DBSCAN
pareto
frontier search
config_diff
nearest twin
recommender
Optuna TPE
One JSON-serialisable payload → dashboard + /export
per-stage timing log · parse stats · every stage independently fault-isolated
Notes: Walk left to right, top to bottom. Key points: the log grammar lives in one module shared by generator and parser so they cannot drift; analysis runs off the request thread so the UI stays responsive; the five analytics stages are independent, so a failure in one still yields a report.

## Slide 5
DATASET
A synthetic corpus we can grade ourselves
Real regression logs come with no answer key. We generated ours, so every discovery can be scored against known truth.
UVM Configuration Intelligence · Team Asterix
05
How the corpus is generated
Grammar first: log_format.py is the single source of truth for the log syntax — the generator writes it and the parser reads it, so the two cannot drift apart.
Vectorised sampling: all 50,000 runs are drawn with NumPy over a weighted configuration space; only the final text rendering loops.
Deliberately lopsided weights so the model faces a realistic, imbalanced design space rather than a uniform grid.
Failure probability is composed rule-by-rule, then the verdict, error trace, UVM report summary and metrics are rendered to match.
Base failure probability is fixed at 1.2 % so a clean configuration sits below the 2 % ceiling the recommender optimises against.
python -m uvm_intel.generate_logs --n-runs 50000 --parts 10
Verdict split across 50,000 runs
Chart: 
| Pass | Fail
Verdict | 75.96 | 24.04
11
configuration knobs
2
environment readings
8
UVM test sequences
7
error-tag taxonomy
4
outcome metrics
~56 MB
corpus, 10 files
Notes: Config knobs: test_name, cache_policy, test_mode_enabled, queue_depth, num_channels, num_planes, ecc_mode, scrambler_enable, burst_length, clock_freq_mhz, prefetch_depth. Environment: voltage_mv and temperature_c, both normally distributed. Outcomes: execution_time_ms, throughput_mbps, cycles, error tags. Overall failure rate lands at 24.04 %.

## Slide 6
GROUND TRUTH
Seven failure rules, planted on purpose
Written to data/uvm_ground_truth.json at generation time — the pipeline is graded on whether it rediscovers them.
UVM Configuration Intelligence · Team Asterix
06
Rule | Condition | Effect on failure | Runs | Fail rate | Lift
R1 | test_name = Back_To_Back_Program + cache_policy = Adaptive | set 0.85, FIFO_OVERFLOW | 2,891 | 0.851 | 4.19×
R2 | test_mode_enabled = 1 | +0.35 | 13,999 | 0.473 | 3.16×
R3 | queue_depth ≥ 32 + ecc_mode = Disabled | +0.35, ECC_UNCORRECTABLE | 1,976 | 0.574 | 2.53×
R4 | temperature_c > 85 + voltage_mv < 1100 | +0.30, RETENTION_FAIL | 281 | 0.559 | 2.34×
R5 | num_planes = 4 + burst_length = 64 + scrambler_enable = 1 | set 0.98, deterministic | 815 | 0.987 | 4.33×
R6 | clock_freq_mhz ≥ 1000 + prefetch_depth > 8 | +0.30, TIMEOUT | 8,014 | 0.475 | 2.43×
R7 | cache_policy = Disabled + queue_depth ≥ 16 | +0.30, DATA_MISMATCH | 2,800 | 0.493 | 2.19×
R5
The planted RTL bug
R5 emits a byte-identical error trace on every hit, whatever the seed. It is the target the fingerprinting stage has to isolate from ordinary flakes.
✓
Graded, not guessed
R1 and R2 are the two rules named in the problem brief.
Every lift figure shown is measured on the corpus, not assumed.
Any future model change is re-scored against the same answer key.
Notes: Lift = failure rate when the rule fires ÷ failure rate when it does not. R4 is deliberately rare (281 runs) to test whether the pipeline can still find a low-support but high-lift rule.

## Slide 7
MODEL
Failure-risk classifier with SHAP attribution
LightGBM gradient boosting on configuration knobs only — the settings an engineer can actually change.
UVM Configuration Intelligence · Team Asterix
07
Design decisions that matter
Leakage guard: every outcome column — execution_time_ms, throughput_mbps, cycles, UVM error counts, verdict, error tags, traces — is excluded from the feature set by construction.
seed and run_id are dropped too: a seed is not a setting anyone can ship.
Categorical knobs are cast to pandas category and handled natively by LightGBM — no one-hot blow-up.
SHAP TreeExplainer gives global importance and per-value attribution, so the output is 'cache_policy = Adaptive raises risk', not just 'cache_policy matters'.
Held-out split reports ROC-AUC, average precision, accuracy, F1, ROC curve and confusion matrix — all surfaced in the dashboard.
0.88
Typical held-out ROC-AUC
on the bundled 50k corpus
Signal strength the model has to learn
Observed failure-rate lift per embedded rule
Chart: 
| R7 | R4 | R6 | R3 | R2 | R1 | R5
Lift | 2.19 | 2.34 | 2.43 | 2.53 | 3.16 | 4.19 | 4.33
Notes: The leakage guard is the point to dwell on: it is trivial to score 0.99 by feeding the model uvm_error_count, and completely useless — the model would be reading the answer. Restricting features to settable knobs is what makes the SHAP ranking actionable.

## Slide 8
ANALYTICS ENGINE
Four techniques behind the four analysis tabs
UVM Configuration Intelligence · Team Asterix
08
A
Failure fingerprinting
Every error message is masked to a seed-invariant template — 0x0004a2c0 → <ADDR>, 32 → <N>.
TF-IDF is fitted over distinct templates, not runs: a 50k corpus collapses to ~7 templates, so DBSCAN stays trivial.
determinism = 1 − (distinct raw traces ÷ runs in cluster).
c1 n=804 PROTOCOL_VIOLATION det=0.999 → deterministic RTL bug
c2 n=3040 TIMEOUT det=0.000 → seed-dependent noise
B
Trade-off frontier
Pareto frontier over throughput versus predicted risk.
Points are grouped on the top-4 SHAP-ranked discrete settings — continuous readings would make every run its own configuration.
Yields 318 configurations of 3–109 runs each.
Predicted risk tracks observed failure rate: 0.139 vs 0.139.
C
Recommender
Optuna TPE search over two surrogates: the risk classifier and a throughput regressor fitted on passing runs only.
Objective is 'throughput when it works', not throughput averaged with degraded failures.
Maximise throughput subject to predicted risk ≤ 2 %, applied as a penalty so TPE learns the constraint shape.
If the ceiling is unreachable the API says so and returns the lowest-risk configs found.
D
Config diff
Aggregate delta: how each setting's distribution shifts between passing and failing runs.
Nearest-twin: each failing run is paired with its most similar passing run, recording exactly which settings differ.
Both views are scoped to identical test sequences.
Numeric fields only count as changed at ≥ 0.5 SD — otherwise voltage and temperature bury the settings that matter.
Notes: The determinism score is the headline result: 804 runs, 804 different seeds, one distinct raw trace. That is exactly the separation between a real RTL bug and seed noise that the brief asks for. min_samples=1 in DBSCAN is intentional — a template seen once is a rare bug, not noise to discard.

## Slide 9
DASHBOARD · TAB 1 OF 7
Executive Summary
The one screen a lead opens first: how bad is this regression, and what is driving it?
UVM Configuration Intelligence · Team Asterix
09
INSERT SCREENSHOT
Executive Summary tab — full view
Capture the whole tab at 1440 px wide after running the bundled sample
What is on this screen
KPI strip — runs parsed, pass/fail counts, failure rate, error lines.
Pass/fail donut and a risk-band histogram of predicted failure probability.
Global SHAP importance chart — the ranked cause list.
Failure-mode distribution across the seven error tags.
ROC curve, held-out metrics and confusion matrix for the risk model.
Mean execution time broken down by failure mode.
Notes: Demo tip: open with the bundled sample so the page is already populated. Point at the SHAP chart and name the top knob, then move to the failure-mode distribution.

## Slide 10
DASHBOARD · TABS 2–3 OF 7
Failure Fingerprints · Trade-off Matrix
UVM Configuration Intelligence · Team Asterix
10
INSERT SCREENSHOT
Failure Fingerprints tab
Show the cluster map with a high-determinism cluster selected
INSERT SCREENSHOT
Trade-off Matrix tab
Show the Pareto scatter with the knee point highlighted
★
Failure Fingerprints
SVD cluster map — each point a failure cluster, sized by run count.
Cluster table with determinism score, run count, distinct seeds and distinct raw traces.
Drill-down showing the masked template beside a raw trace.
One-click hand-off into the diff viewer for any clustered run.
★
Trade-off Matrix
Interactive throughput-versus-risk scatter with the frontier drawn through it.
Three named operating points: peak throughput, knee, and best-safe.
Full frontier table with observed and predicted failure rate per configuration.
Hover any point to read the exact configuration behind it.
Notes: Fingerprints is the tab to spend the most demo time on — sort the cluster table by determinism and show the near-1.0 cluster, then open the drill-down to prove the traces are identical.

## Slide 11
DASHBOARD · TABS 4–7 OF 7
Recommendations · Config Diff · Run Explorer · All Details
UVM Configuration Intelligence · Team Asterix
11
INSERT SCREENSHOT
Recommendations tab
Show the top recommended config and the Optuna history plot
▸
Recommendations
Ranked configurations from the TPE search with predicted throughput and risk.
Optimisation history across trials.
The derived search space actually explored.
INSERT SCREENSHOT
Config Diff tab
Show the two-run log diff with divergent settings highlighted
▸
Config Diff
Twin-divergence ranking — which settings flip a run from pass to fail.
Interactive two-run log diff viewer.
Closest failing/passing pairs and aggregate deltas per sequence.
INSERT SCREENSHOT
Run Explorer + All Details tab
Show the paged run table, then the parse-stats panel
▸
Run Explorer + All Details
Paged, filterable, sortable table of every parsed run.
Parse stats, per-stage timing log, failure rate by field with lift.
Metric distributions, highest-risk runs, job metadata, column inventory.
Every tab reads from the same job payload, and the whole report can be downloaded as JSON from /api/jobs/{id}/export.
Notes: Keep this section brisk in the demo — one sentence per tab, then return to Fingerprints for questions.

## Slide 12
ENGINEERING
Software stack, API surface and measured performance
UVM Configuration Intelligence · Team Asterix
12
Frontend
React 18 · Vite 5 · Recharts · Axios
Custom dropzone, polling job client, 7 tab views
Backend
FastAPI 0.104 · Uvicorn · python-multipart
Threaded job registry, CORS, 512 MB upload cap
ML & analytics
LightGBM · SHAP · scikit-learn · Optuna (TPE)
TF-IDF + DBSCAN · NumPy · pandas
Tooling
Python 3.11 · pytest parser suite · CLI entry points
Shared log grammar module, ground-truth grader
REST API
GET /api/health liveness + bundled-sample availability
POST /api/analyze upload .log files, start a job
POST /api/analyze-sample analyse the bundled corpus
GET /api/jobs/{id} status + progress
GET /api/jobs/{id}/result full analysis payload
GET /api/jobs/{id}/runs paged run table
GET /api/jobs/{id}/diff field-by-field diff of two runs
GET /api/jobs/{id}/export download payload as JSON
Measured performance
Corpus | Parse | Full analysis
5,000 runs | ~0.6 s | 9.6 s
10,000 runs | ~1.2 s | 27 s
50,000 runs | 2.0 s | —
Python 3.11, 8 cores. 1,015,872 lines parsed with zero malformed blocks and zero unparsed lines. Job-level tunables: max_risk, n_trials, dbscan_eps, enable_recommender.
Notes: If asked why a worker thread rather than a process pool: the heavy stages release the GIL (NumPy, LightGBM), and a thread keeps the job registry and progress callback in one address space.

## Slide 13
ROADMAP
Future scope
Ordered by the value each item adds against the effort it needs.
UVM Configuration Intelligence · Team Asterix
13
Near term
1
RAG copilot
ChromaDB + LangChain natural-language Q&A over the parsed corpus — scoped in the plan, deferred because it needs an LLM endpoint and key.
2
Regression-over-time
Persist jobs to a database and trend failure rate, SHAP ranking and cluster membership across nightly runs.
3
CI integration
A gate that fails the build when a new deterministic cluster appears or predicted risk crosses the ceiling.
Longer term
1
Real log adapters
Pluggable grammars for VCS, Questa and Xcelium output so the pipeline runs on production regressions, not just the synthetic corpus.
2
Coverage-aware recommendation
Add functional-coverage closure as a third objective beside throughput and risk.
3
Automatic triage routing
Map each fingerprint cluster to an owning component and open the ticket with the twin-diff attached.
4
Live streaming ingest
Consume logs as the regression runs, so risky configurations are flagged mid-flight instead of at the end.
Notes: Be straight about the RAG copilot: it was a listed bonus, it is not built, and the reason is a product decision about an LLM endpoint rather than a technical blocker. Everything else in the plan is in place.

## Slide 14
IN CLOSING
From a million log lines
to one recommended configuration
Parsed
1,015,872 lines in 2.0 s, zero malformed blocks — ingestion is not the bottleneck.
Explained
Leakage-controlled LightGBM with SHAP names the knobs, not just the symptoms.
Separated
A determinism score isolates a real RTL bug from 3,000 seed-dependent flakes.
Recommended
Optuna TPE returns the fastest configuration that still meets a 2 % risk ceiling.
Thank you · Questions
Team Asterix · SanDisk Hackathon 2026
Notes: Close on the determinism result — it is the most distinctive thing the project does.